## Slide 1: Automating As-Built and GIS Data Requests
Michael Hanson
GIS/Asset Management Technician
City of Rosemount

## Slide 2: Overview
Background
Request for Automated Tool
Challenges
  Other Options and Considerations
  Permissions Handling
Solution
  Survey123
  Power Automate
  Python
Tracking
Github: Code/PPT

## Slide 3: Background – Plan area layer
Utility as-built pages are extracted, stamped, and their extent digitized to a ‘Plan Areas’ layer
Each page is saved to a Sharepoint folder with name format:
  {as-built #}.pdf
A hyperlink concatenates automatically in the Plan Areas layer using attribute rules
Github: Code/PPT
Notes: Each page of every as-built we receive is stamped with an as-built number. The extent of that page is added to a Plan Areas feature class, which allows spatial and/or attribute querying of as-built records.

## Slide 4: Plan Area Layer – As-Built Extractor Tool
Python modules: PyPDF2, reportlab, fitz, PIL, customtkinter
https://github.com/m-hanson-5/PDF_Extractor
Stamps specified pages with sequential as-built numbers
Extracts each page to pdf
Saves pdf’s to Sharepoint directory (optional)
Produces JPEG’s (optional)

## Slide 5: Plan area layer - Fields
Field Schema:
  ID (As-Built #; this field is used to relate to other layers’ as-built references)
  Hyperlink
  Water (y/n)
  Sanitary (y/n)
  Storm (y/n)
  Grading (y/n)
  Project Number
  Project Name
  Install Year
  Plan Type (Record Drawing, Construction Plan, Private Plan)
Github: Code/PPT

## Slide 6: Plan area layer – Attribute Rules
Github: Code/PPT
Notes: Plan Areas are a place to store project level data that can be absorbed by other features referencing that as-built

## Slide 7: The Tool
Requirements:
  Web interface. No login needed
  Tool accepts a polygon input
  Validation process to ensure requester has permission to access data
  Output is an emailed link to a Sharepoint folder with as-built pdf’s and GIS files (if specified)
Github: Code/PPT

## Slide 8: Challenges
Process begins online but must access local files
Permissions Handling
  SOLUTIONS CONSIDERED:
  Add script to a toolbox and share as a Web Tool (Geoprocessing Service)
    Difficult to customize without Javascript, same issue of file management from web tool
  Power Automate Premium
    Allows use of Power Automate Desktop in ‘unattended mode’
    Can run a local script in response to a trigger
    $$$
  ✅ Python script on a polling interval using Task Scheduler
Github: Code/PPT

## Slide 9: WORKFLOW
User draws a polygon
in Survey123
Survey123
Power Automate
Python
Power Automate detects the submission
  Sends an email to the user
  acknowledging submission
  Creates a GIS Ticket for tracking
Python script polls for changes to the Survey123 layer and processes the request
Github: Code/PPT

## Slide 10: Survey123
As-Built Download Request Form
Github: Code/PPT

## Slide 11: Power Automate Flow
Note: the final email with the link to the files comes from Python script
Github: Code/PPT

## Slide 12: Example of Email to GIS HelpDesk
A new request with request id 200004367 has been created by Public Works. Short info on the request is : Title : A new as-built download request has been submitted. Category : Description :A new as-built download request has been submitted.
Requestor Email:<derick.anderson@rosemountmn.gov>
Desired Output Location: <DCTC>
Global ID: {DD597079-7605-46B6-8CC6-194F0E5BFA98}
You may fulfill the download request immediately by running the below script:
\Automation\As-Built_Auto_Downloader.py
As-Built Request Tracker
Github: Code/PPT

## Slide 13: Python
Python modules: arcpy, pandas, logging
https://github.com/m-hanson-5/As-Built-Downloader
View Code on GitHub:
Github: Code/PPT
Notes: Logging and error handling with try/except blocks and email alerts

## Slide 14: Python
Github: Code/PPT

## Slide 15: Python
Github: Code/PPT

## Slide 16: Python – Managing Fields Shared in GIS Files
Github: Code/PPT

## Slide 17: Task Scheduler – Silent Operation
Method with a .vbs file below, though .bat is also possible
vbs file content:
Task Scheduler:
Set WshShell = WScript.CreateObject("WScript.Shell") WshShell.Run """C:\Program Files\ArcGIS\Pro\bin\Python\envs\arcgispro-py3\python.exe"" ""C:\Users\mdh\OneDrive - ci.rosemount.mn.us\GIS Projects\Automations\As-Built_Auto_Downloader.py""", 0
Path to .vbs file
.vbs file
Alternatives for silent operation:
‘Run whether user is logged in or not’
Pythonw.exe
‘start /B’ in .bat file
Github: Code/PPT

## Slide 18: Tracker App
Experience Builder app to track open tickets
As-Built Download Request Tracker

## Slide 19: Questions?
Github: Code/PPT